## Slide 1
MRSP Project Group 8
Group Members:
Farzeel Aftab
Tatiana Merkulova
Aftab Arshad Muhammad Jawad Asghar

## Slide 2: Task 1
Audio Data
    24-bit, 44100 kHz sound files
Dataset
    5 original audio files
    15 derivative audio files across 3 acoustic environments: Opera Hall, Reverberation Hall, Small Office
Software Used
    Free Sound
    Audacity

## Slide 3: Task 2
Objective
    Analyze and compare perceived quality of audio files after applying two compression methods: Uniform Quantization and AAC Encoding.
Compression Methods:
Uniform Quantization
    Divides continuous range of amplitudes into finite levels.
    Reduces bit depth, leading to compression.
AAC Encoding
    Advanced Audio Coding with better sound quality than MP3 at similar bit rates.
    Utilizes perceptual noise shaping and predictive coding.

## Slide 4: Perceived Quality Loss - Results Overview
Measured for both Quantization and AAC Encoding.

## Slide 5: Key Findings:
Quantization results in higher perceived loss than AAC encoding in most cases.
AAC consistently maintains better sound quality (Ratio < 1).
Observations by Genre:
Walking on Leafs:
    AAC shows significantly lower PLOSS values compared to Quantization.
    Ratio ranges from 0.0959 to 0.1101.
Smoothie:
    Mixed results; some files show higher PLOSS with AAC.
    Ratios up to 1.2292, indicating higher perceived loss in some cases.

## Slide 6
Observations by Genre: (continue)
Drum Kit & Traffic::
    AAC consistently outperforms Quantization
    Significantly lower PLOSS values, e.g., Drum Kit (Ratio 0.0874 - 0.6366),
    Traffic (Ratio 0.0351 - 1.0165)
Drums:
    AAC better preserves sound quality.
    Ratios range from 0.0280 to 0.0540

## Slide 7: Conclusion
Overall Analysis:
    Quantization leads to greater perceived loss compared to AAC.
    Ratios (AAC/Quantized) < 1 for most audio files, highlighting AAC’s effectiveness
Genre-Specific Observations:
    "Smoothie" genre exhibits higher perceived loss with AAC in some cases..
    "Drum Kit," "Traffic," and "Drums" genres show AAC significantly outperforms Quantization.

## Slide 8: Result Graphs plotted using the results from the MUSHRA Test.